## Slide 1: Introduction to tespy
Master Course
2025-04-28

## Slide 2: tespy architecture
Basics
  Network
  Components
  Connections
  How to build, parametrize and run models?
Advanced
  Buses
  UserDefinedEquations
  Plotting of cycle and heat exchanger diagrams
Overview
To warm up your keyboards:
  Update your environment (tespy and CoolProp updates were published)
  pip install tespy --upgrade

## Slide 3: Hands-on: Simple heat pump model
Build up a heat pump model with the following specifications
  Evaporation temperature: 15 °C
  Condensation temperature: 60 °C
  Working fluid: R290
  Compressor efficiency: 85 %
  Disregard pressure drops in heat exchangers
What is the role of the cycle closer?
Tasks

## Slide 4: Hands-on: Results processing
What is the COP of the heat pump?
Plot the logp-h diagram of the cycle
  Show the state points
  Connect them with the respective process lines
  Remember thermodynamics 101: What should be noted when drawing process lines?
Tasks

## Slide 5: Hands-on:
Extend the model by integrating material flow for the heat source and the heat sink
  Air on heat source side
  Water on heat sink side
  What are reasonable assumptions for the heat exchangers?
Plot the TQ-diagram of the condenser and discuss, what issues might arise?
Tasks

## Slide 6: Hands-on: Heat pump model
Run a sensitivity analysis on the COP:
  As a function of ambient temperature
  As function of heat sink temperature
  For a variety of working fluids
Tasks

## Slide 7: Hands-on: Heat pump model
At what heat sink temperature is the COP of the heat pump exactly
  4
  5
  …
What methods other than trying manually do you recall to implement this?
  Remember: This is an equation based solver!
Tasks

## Slide 8: Next Time: Gas turbine
Repeat the concepts and syntax of tespy
What can we do, if the solver returns a linear dependency?
In what (numerical) issues did we run and how did we solve them?
How can we make use of component error messages?
Things to prepare