## Slide 1: Thermodynamic cycles II: Organic Rankine Cycle
Master Course
2025-05-12

## Slide 2: Low temperature heat utilization
Simple Cycle
  Building a model
  Changing fluids
  Processing results
Typical working fluids
  Characteristics
  Plotting of fluid properties
Advanced cycle
  Recuperated cycle
Overview
Parametric study
  Recuperator sizing
  Turbine inlet temperature

## Slide 3: Simple ORC
Heat source
  100 kg/s of air
  Temperature: 160 °C
  Pressure: 1 bar
Heat sink
  Fluid: air
  Temperature: 20 °C, air temperature increase: 15 K
  Pressure: 1 bar
Cycle
  Working fluid: water
  Condenser outlet: saturated liquid
  Evaporator inlet: saturated liquid
  Evaporator outlet: saturated gas, 140 °C
Components
  Pump efficiency: 75 %
  Turbine efficiency: 85 %
  Evaporator lower terminal temperature diff: 5 K
  Condenser lower terminal temperature diff: 15 K
  Disregard pressure drops in heat exchangers
Build an ORC model with the following specifications

## Slide 4: Simple ORC
Analyse the plant’s performance
  Calculate the power generation
  Calculate the thermal efficiency
  Plot the cycle’s T-s diagram and include a plot of the saturation lines
Change the fluids
  Use isopentane as working fluid
  Why does the power output change in comparison with water as working fluid?
Tasks
Analyse the performance
  Plot the cycle’s T-s diagram
  Plot the condenser’s Q-T diagram
Replace the condenser by with the MovingBoundaryHeatExchanger model
  Impose a minimum pinch temperature difference of 5 K
Replace the heat source fluid with water at 10 bar

## Slide 5: Working fluids
Typical working fluids are, e.g.:
  Isopentane
  cyclopentane
Plot the T-s diagrams of these working fluids and compare it to water
What could be reasons, water is NOT typically used in low-temperature heat regimes?
Tasks

## Slide 6: Working fluids
Make use of the fluprodia library to create the T-s diagrams of isopentane
Include a plot of the process in it using fluprodia‘s interface for process lines
Tasks

## Slide 7: Advanced cycles
Add an internal recuperator to your model and find a feasible solution for the problem
  Impose a value of 0.5 for the heat exchanger hot side effectiveness
What does the internal heat exchanger change?
  Power output?
  Thermal efficiency?
  …?
Tasks

## Slide 8: Parametric analyses
How does the performance of the cycle change for different sizes of the heat exchanger?
  Change the size of heat exchanger by modifying the effectiveness between 0.05 and 0.95
How does the turbine inlet temperature affect the power output?
  Calculate the power output for a temperature range from 80 to 150 °C
Recuperated cycle configuration analysis
What is the recuperator size under the following conditions
  Turbine inlet temperature: 100 °C
  Heat source outlet temperature: 80 °C

## Slide 9: Next Time: Design/Offdesign
What parameters characterize different components: Once you the actual component was manufactured, what quantity cannot change anymore? Think about
  Heat Exchangers
  Turbines
  Pumps
  Compressors
Things to prepare