## Slide 1: Cycles III: CHP
Master Course
2025-05-26

## Slide 2: Cycles III
Combined Heat and Power Generation
New Components
Build up cycles and change configuration stepwise
Explore complex part load behaviour
Content

## Slide 3: Cycles III
Saves fuel in comparison to conventional technologies
Becomes less important with phase out of thermal power plants
May be a backup technology for times with low renewable generation in heating period
Combined Heat and Power Generation

## Slide 4: Cycles III
CHP Options for Gas Turbines or arbitraty fuels

## Slide 5: Cycles III
Extraction turbine
Set up a simple CHP plant:
  Life Steam: 100 bar/500°C
  Heating condenser at 90 °C
  Cooling water at 20°C
  Net power output: 50 MW
  Heating Power 50 MW
  Turbomachinery efficiency: 90 %
  Steam generator pressure loss: 10 %
Find missing info, do it stepwise!
c01
c02
c03
c04
c11
c12
c13
a01
a02

## Slide 6: Cycles III
New TESPy components
Condenser:
  Heat Exchanger
  Includes condition of saturated liquid at hot side outlet
  Temperature differences
Bus:
  Allows to summarize power outputs and inputs including electro-mechanical efficiencies
Splitter and Merge
c01
c02
c03
c04
c11
c12
c13
a01
a02

## Slide 7: Cycles III
Extraction turbine
Expand heating condenser to two-sided model
Test part load behaviour for different life steam mass flows at constant cooling water and district heating return temperatures and mass flows
(switch to off-design component-wise!)
Visualize results
c01
c02
c03
c04
c11
c12
c13
a01
a02

## Slide 8: Cycles III
For those who can‘t get enough
  Try changing district heating duty
  Introduce a valve to control forward temperature (twice)
  Set up a cycle to produce steam with gas turbine exhaust gases
Next unit
  Optimization with TESPy
Next steps