## Slide 1: Exam Preparation
Master Course
2025-06-16

## Slide 2: Exam Preparation
Organization
Exam Conditions
Example Exercises
Overview

## Slide 3: Exam Preparation
Exam to be taken in FUAS‘ exam week
Possible Dates (priotities):
  Tuesday, July 1st: 10:00 – 12:00 (1)
  Wednesday, July 2nd, 13:00 – 15:00 (4)
  Thursday, July 3rd, 13:00 – 15:00 (3)
  Friday, July 4th, 10:00 – 12:00 (2)
Organization

## Slide 4: Exam Preparation
Exam will be taken in computer lab
Exercises will be handed out as paper copies including whitespace for written answers or sketches
Python scripts will be available locally on computers
Computers will have no network connection
TESPy documentation will be available locally
Exam Conditions

## Slide 5: Exam Preparation
a) Air Compressor File: ep_01_a.py
b) Piping File: ep_01_b.py
Code with Errors
c1
c2
c1
c2
b) Turbine File: ep_01_c.py
c1
c2

## Slide 6: Exam Preparation
The better it is documented the easier it is to understand code!
Demonstrate that you can read TESPy code written by others.
File: ep_02.py
  Sketch a HBD
  Explain what the code is for
  Improve the code introducing comments and/or better nomenclature
Understand Code

## Slide 7: Exam Preparation
The file ep_03.py contains a script to simulate the recuperated closed cycle gas turbine depicted on the right
Use the existing script to determine the optimum compressor pressure ratio with respect to the cycle efficiency
Stick to all other given parameters
Recuperated Closed Cycle Gas Turbine
c1
c2
c3
c4
c5
c6
c7

## Slide 8: Exam Preparation
Set up the flash process depicted on the right in a respective TESPy network
Parametrize your model in order to determine the vapor content at the end of the process
  c1: water at 1 bar and 20 °C
  c3: boiling water at 200 °C
  c4: flash pressure 1 bar
  Pump efficiency: 75 %
  HX pressure drop: 5 %
Flash Process
c1
c2
c3
c4

## Slide 9: Next step: Exam
Yourself:
  Find and tackle issues in TESPy code
  Documentation of TESPy code
  Modify TESPy code written by others
  Gerenate own TESPy code to solve problems in thermal process engineering
Things to prepare